## Slide 1: PVLAN & PVLAN over EVPN VXLAN
EMEA SE Call
2021 06 14
Angelique Phillipps
Khelil Sator
Notes: K

## Slide 2: Agenda
PVLAN
  Definition
  Trunk Mode
  Arista Support
PVLAN over EVPN VXLAN
  Control Plane and Data Plane
  Traffic Flow
  Arista Support
Notes: K

## Slide 3: PVLAN
Notes: K

## Slide 4: Private VLAN
Private VLANs are a collection of VLANs
  There is a single primary VLAN, and one or more secondary VLANs
Primary VLAN
  Ports in the primary VLAN can send/receive traffic from ports in all the corresponding PVLANs
  There will only be one primary VLAN in a private VLAN Domain
Secondary VLAN
  Community VLAN
    Hosts in the same community VLAN can forward traffic to each other as well as ports in the primary VLAN
    There can be multiple community VLANs in a private VLAN
  Isolated VLAN
    Hosts in an isolated VLAN can only forward traffic to ports in the primary VLAN
    Hosts within an isolated VLAN are not allowed to communicate with each other via bridging
Notes: K

## Slide 5: PVLAN Ports
Promiscuous port
  All ports in primary VLAN are called promiscuous ports
  By default all promiscuous ports are mapped to all secondary VLANs
  Communicates with anything else connected to the primary or any secondary VLAN
  Connects to a router, firewall or other common gateway device
Host port
  Community port
    Connects to the host that resides on community VLAN
    Communicates with promiscuous ports and ports on the same community VLAN
  Isolated port
    Connects to the host that resides on isolated VLAN
    Communicates only with promiscuous ports
Notes: K

## Slide 6: PVLAN Traffic Flow
Src Dest | Primary VLAN 10 | Isolated VLAN 11 | Community VLAN 12 | Community VLAN 13
Primary VLAN 10 | OK | OK | OK | OK
Isolated VLAN 11 | OK | NOK | NOK | NOK
Community VLAN 12 | OK | NOK | OK | NOK
Community VLAN 13 | OK | NOK | NOK | OK
VLAN 13
VLAN 12
VLAN 11
VLAN 10
Notes: K

## Slide 7: PVLAN Configuration
platform sand l2 forwarding-id sharing
!
!
vlan 10
!
vlan 11
private-vlan isolated primary vlan 10
!
vlan 12-13
private-vlan community primary vlan 10
!
interface Ethernet 27/1
switchport access vlan 11
!
interface Ethernet 28/1
switchport access vlan 12
!
interface Ethernet 33/1
switchport access vlan 10
show vlan private-vlan
Primary Secondary Type Ports
------- --------- ----------- --------
10 12 community Et28/1, Et33
10 13 community Et33
10 11 isolated Et27/1, Et33
show vlan
VLAN Name Status Ports
----- ------ -------- ----------------------
1 default active
10 VLAN0010 active Et27/1+, Et28/1+, Et33
11 VLAN0011 active Et27/1, Et33+
12 VLAN0012 active Et28/1, Et33+
13 VLAN0013 active Et33+
+ indicates a private VLAN promoted port
Primary VLAN
Secondary VLAN
Secondary VLAN
On Sand Platforms
Promiscuous Port
Host Port
Host Port
Notes: K

## Slide 8: MAC Learning in Primary VLAN
s70515#sh run int ethernet 27/1,28/1
interface Ethernet27/1
switchport access vlan 11
interface Ethernet28/1
switchport access vlan 12
!
!
!
!
s70515#sh mac address-table
VLAN Mac Address Type Ports Moves Last Move
---- ----------- ---- ----- ----- ---------
10 985d.82b4.ca61 DYNAMIC Et27/1 1 0:00:43 ago
10 985d.82b4.ccf5 DYNAMIC Et28/1 1 0:03:58 ago
Total Mac Addresses for this criterion: 2
Secondary VLAN
Secondary VLAN
Primary VLAN
Notes: K

## Slide 9: Mapping on a Promiscuous Port
s70515#show running-config interfaces ethernet 33
interface Ethernet33
switchport access vlan 10
s70515#show vlan
VLAN Name Status Ports
--- --------- -------- ------------------------------
1 default active
10 VLAN0010 active Et27/1+, Et28/1+, Et33
11 VLAN0011 active Et27/1, Et33+
12 VLAN0012 active Et28/1, Et33+
13 VLAN0013 active Et33+
+ indicates a private VLAN promoted port
By default a promiscuous ports is mapped to all secondary VLANs
s70515#show running-config interfaces ethernet 33
interface Ethernet33
switchport access vlan 10
switchport pvlan mapping 1-11,13
s70515#show vlan
VLAN Name Status Ports
--- -------- ---------- ----------------------------
1 default active
10 VLAN0010 active Et27/1+, Et28/1+, Et33
11 VLAN0011 active Et27/1, Et33+
12 VLAN0012 active Et28/1
13 VLAN0013 active Et33+
+ indicates a private VLAN promoted port
Without explicit mapping
With mapping
Notes: K

## Slide 10: PVLAN and Trunk Mode
Regular trunk mode
  PVLAN (primary and secondary VLANs) are supported on the trunk as long as they are allowed
  No Private VLAN specific behaviour on this trunk
  Frames are forwarded towards the trunk the way they have been received by the switch in terms on VLAN tag (for primary and secondary VLANs)
  The device connected to the trunk must be PVLAN aware for the frame to be handled accordingly on the destination device
  Use case:
    Interconnecting 2 PVLAN-aware devices
Host
in vlan 10
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Host
in vlan 10
Host
in vlan 13
Host
in vlan 13
Host
in vlan 11
Trunk
PVLAN aware
PVLAN aware
Notes: A

## Slide 11: PVLAN and Trunk Mode
Promiscuous trunk mode
  Not supported by Arista
  When traffic from a secondary VLAN needs to pass over the trunk, the secondary VLAN tag is rewritten with the primary VLAN tag
  Use case:
    Communication with PVLAN-unaware devices
    An external router on a stick routes between several primary VLANs
Host
in vlan 10
First Private VLAN Domain
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Second Private VLAN Domain
Primary VLAN:20
Community VLAN: 21
Isolated VLAN: 22
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Host
in vlan 13
Host
in vlan 11
Host
in vlan 20
Host
in vlan 21
Host
in vlan 22
Host
in vlan 21
Host
in vlan 22
Trunk
Host
in vlan 13
Host
in vlan 11
Host
in vlan 21
Host
in vlan 22
Trunk
NOT PVLAN aware
PVLAN aware
PVLAN aware
Notes: A
No hosts in secondary VLANs on PVLAN unaware devices

## Slide 12: Workaround for Promiscuous Trunk
VLAN translation on trunk interface
  Egress VLAN translation on the trunk for all secondary VLANs to primary VLAN
Configuration Example
interface Ethernet 1
switchport mode trunk
switchport vlan translation out 11-13 10
switchport vlan translation out 21-23 10
Configuration on the access port in secondary VLAN unchanged
Keep the configuration synchronized between trunk and PVLAN Domain when adding/removing secondary VLANs
E1
Host
in vlan 13
Host
in vlan 11
Host
in vlan 21
Host
in vlan 22
Trunk
PVLAN aware

## Slide 13: PVLAN and Trunk Mode
Secondary VLAN trunk mode
  Arista supported feature
  This option rewrites the primary tag on the frame to use a secondary VLAN ID
  Any frame coming in on a primary VLAN will go out on the trunk with the lowest values secondary VLAN in that private VLAN domain
  Configuration: switchport trunk private-vlan secondary
  Use case:
    Communication with PVLAN-unaware devices
Gateways on PVLAN-aware device
Devices on PVLAN-unaware devices
Trunk
Host
in vlan 11
Host
in vlan 21
Host
in vlan 10
First Private VLAN Domain
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Second Private VLAN Domain
Primary VLAN:20
Community VLAN: 21
Isolated VLAN: 22
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Host
in vlan 20
Host
in vlan 21
Host
in vlan 22
NOT PVLAN aware
PVLAN aware
Notes: A : in the first private vlan domain, if vlan 11 is not allowed on the trunk, the traffic will be dropped as the rule remains the same whether or not the traffic is allowed

## Slide 14: PVLAN and Trunk Mode
Isolated VLAN trunk mode
  Terminology used by other vendors
  This option rewrites the primary tag on the frame to use the isolated VLAN ID
  Any frame coming in on a primary VLAN will go out on the trunk with the isolated VLAN values in that private VLAN domain
  Use case:
    Communication with PVLAN-unaware devices
Gateway on PVLAN-aware device
Hosts on PVLAN-unaware devices
Trunk
Host
in vlan 11
Host
in vlan 22
Host
in vlan 10
First Private VLAN Domain
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Second Private VLAN Domain
Primary VLAN:20
Community VLAN: 21
Isolated VLAN: 22
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Host
in vlan 20
Host
in vlan 21
Host
in vlan 22
PVLAN aware
NOT PVLAN aware
Notes: A
Cisco: uses the isolated VLAN. With Arista can configure several isolated vLANS, with Cisco only one.

## Slide 15: Arista Support for Trunk Mode
Regular trunk mode
  Supported on Arista switches
Promiscuous trunk mode
  Not supported on Arista switches
  VLAN translation as a workaround
Secondary VLAN trunk mode
  Supported on Arista switches
Isolated VLAN trunk mode
  Supported on Arista switches if adequate VLAN numbering
Notes: A

## Slide 16: PVLAN over EVPN VXLAN
Notes: A

## Slide 17: PVLAN over EVPN VXLAN
Spine
Host
in vlan 10
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Host
in vlan 12
Leaf Switches
Spine Switches
EVPN VXLAN Fabric with PVLAN
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Host
in vlan 13
Host
in vlan 11
Host
in vlan 11
Host
in vlan 11
PVLAN behaviour is maintained when stretched across an EVPN VXLAN Fabric
Notes: A

## Slide 18: PVLAN with EVPN VXLAN
Spine
MAC addresses from primary and secondary VLANs
  Only in primary VLAN MAC address-table
  Same behavior as PVLAN without EVPN VXLAN
For route-type 2, MAC and MAC/IP from primary and secondary VLANs are advertised
  With MAC VRF RD/RT of primary VLAN
  With primary VLAN VNI
Route-type 3 are advertised for primary and secondary VLANs
  Hence, flood lists are created for primary and secondary VLANS
VNI encapsulation depends on the source host
Frame is dropped at the destination VTEP when traffic not allowed
Notes: A

## Slide 19: Control Plane and Data Plane
Type 2 (MAC)
RD = 10.1.0.1:10
RT = 10:10
NH = VTEP 1
VNI = 10
MAC = 985d.82b4.ccf5
Host 1
Leaf 1
Spine
Host 2
172.16.0.1
985d.82b4.ccf5
172.16.0.2
444c.a88d.27c1
VNI 12
VNI 10
BGP Update
Leaf 2
Type 2 (MAC)
RD = 10.2.0.2:10
RT = 10:10
NH = VTEP 2
VNI = 10
MAC = 444c.a88d.27c1
BGP Update
Host 3
VNI 11
Type 2 (MAC)
RD = 10.1.0.1:10
RT = 10:10
NH = VTEP 1
VNI = 10
MAC = 985d.82b4.ca61
172.16.0.3
985d.82b4.ca61
Host
in vlan 10
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Notes: A

## Slide 20: Traffic Flow Examples
Spine
Src Dest | Primary VLAN 10 | Isolated VLAN 11 | Community VLAN 12 | Community VLAN 13
Primary VLAN 10 | OK - VNI 10 | OK - VNI 10 | OK - VNI 10 | OK - VNI 10
Isolated VLAN 11 | OK - VNI 11 | NOK - VNI 11 | NOK - VNI 11 | NOK - VNI 11
Community VLAN 12 | OK - VNI 12 | NOK - VNI 12 | OK - VNI 12 | NOK - VNI 12
Community VLAN 13 | OK - VNI 13 | NOK - VNI 13 | NOK - VNI 13 | OK - VNI 13
Notes: A

## Slide 21: Traffic Flow Examples
ping H3 → H2 (OK)
16:30:17.181670 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.18655 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 12
98:5d:82:b4:ca:61 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.3 > 172.16.0.2: ICMP echo request, id 18917, seq 1, length 80
16:30:17.181814 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.20406 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 12
44:4c:a8:8d:27:c1 > 98:5d:82:b4:ca:61, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.3: ICMP echo reply, id 18917, seq 1, length 80
ping H1 → H2 (NOK)
16:36:11.517270 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.54434 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 13
98:5d:82:b4:cc:f5 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.1 > 172.16.0.2: ICMP echo request, id 18969, seq 1, length 80
There is no echo reply.
Host 1
Leaf 1
Host 2
172.16.0.1
985d.82b4.ccf5
Leaf 2
Host 3
172.16.0.3
985d.82b4.ca61
172.16.0.2
444c.a88d.27c1
Community VLAN: 12
Community VLAN: 13
Host
in vlan 12
Host
in vlan 13
VTEP 10.1.1.1
VTEP 10.2.1.2
Notes: A

## Slide 22: Lab Details for the Next Slides
Host 1
Leaf 1 (VTEP)
Spine
Host 2
172.16.0.1
985d.82b4.ccf5
172.16.0.2
444c.a88d.27c1
Leaf 2 (VTEP)
Host 3
172.16.0.3
985d.82b4.ca61
Host
in vlan 10
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
E28/1
E28/1
E28/1
E27/1
E33
E1
E53/1
E27/1
10.0.0.0/31
AS: 65001
Loopback0: 10.1.0.1
Loopback1: 10.1.1.1
VLAN 10: 172.16.0.254/24
AS: 65002
Loopback0: 10.2.0.2
Loopback1: 10.2.1.2
VLAN 10: 172.16.0.254/24
Devices configuration and show commands: https://gitlab.aristanetworks.com/emea-se-team/pvlan_evpn_vxlan
Notes: k

## Slide 23: VLAN Table and VXLAN Address Table
leaf1#show vlan
VLAN Name Status Ports
----- -------------------------------- --------- -------------------------------
1 default active
10 VLAN0010 active Cpu, Et27/1+, Et28/1+, Vx1
11 VLAN0011 active Cpu, Et27/1, Vx1
12 VLAN0012 active Cpu, Et28/1, Vx1
13 VLAN0013 active Cpu, Vx1
+ indicates a private VLAN promoted port
leaf1#
leaf1#show vlan private-vlan
Primary Secondary Type Ports
------- --------- ----------- -------------------------------
10 12 community Cpu, Et28/1, Vx1
10 13 community Cpu, Vx1
10 11 isolated Cpu, Et27/1, Vx1

## Slide 24: VLAN Table and VXLAN Address Table
Leaf2#show vlan
VLAN Name Status Ports
----- -------------------------------- --------- -------------------------------
1 default active
10 VLAN0010 active Cpu, Et53/1, Vx1
11 VLAN0011 active Cpu, Et53/1+, Vx1
12 VLAN0012 active Cpu, Et53/1+, Vx1
13 VLAN0013 active Cpu, Et53/1+, Vx1
+ indicates a private VLAN promoted port
Leaf2#show vlan private-vlan
Primary Secondary Type Ports
------- --------- ----------- -------------------------------
10 12 community Cpu, Et53/1, Vx1
10 13 community Cpu, Et53/1, Vx1
10 11 isolated Cpu, Et53/1, Vx1

## Slide 25: PVLAN over EVPN VXLAN Configuration
router bgp 65002
...
!
vlan 10
rd 10.2.0.2:10
route-target both 10:10
redistribute learned
!
vlan 11
rd 10.2.0.2:11
route-target both 11:11
!
vlan 12
rd 10.2.0.2:12
route-target both 12:12
!
vlan 13
rd 10.2.0.2:13
route-target both 13:13
interface Vxlan1
vxlan source-interface Loopback1
vxlan udp-port 4789
vxlan vlan 10 vni 10
vxlan vlan 11 vni 11
vxlan vlan 12 vni 12
vxlan vlan 13 vni 13
VLAN and port configuration is the same as in PVLAN configuration without EVPN VXLAN
Primary and Secondary VLAN/VNI mapping
Learned MAC redistribution only on Primary VLAN
MAC VRF for all
Primary and Secondary VLANs
Notes: K

## Slide 26: EVPN Route-Type 3
Leaf1#sh bgp neighbors 10.2.0.2 evpn advertised-routes route-type imet detail
Router identifier 10.1.1.1, local AS number 65001
BGP routing table entry for imet 10.1.1.1, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
65001
10.1.1.1 from - (0.0.0.0)
Origin IGP, metric -, localpref 100, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10
PMSI Tunnel: Ingress Replication, MPLS Label: 10, Leaf Information Required: false, Tunnel ID: 10.1.1.1
BGP routing table entry for imet 10.1.1.1, Route Distinguisher: 10.2.0.1:11
Paths: 1 available
65001
10.1.1.1 from - (0.0.0.0)
Origin IGP, metric -, localpref 100, weight 0, valid, local, best
Extended Community: Route-Target-AS:11:11 TunnelEncap:tunnelTypeVxlan
VNI: 11
PMSI Tunnel: Ingress Replication, MPLS Label: 11, Leaf Information Required: false, Tunnel ID: 10.1.1.1
BGP routing table entry for imet 10.1.1.1, Route Distinguisher: 10.2.0.1:12
Paths: 1 available
65001
10.1.1.1 from - (0.0.0.0)
Origin IGP, metric -, localpref 100, weight 0, valid, local, best
Extended Community: Route-Target-AS:12:12 TunnelEncap:tunnelTypeVxlan
VNI: 12
PMSI Tunnel: Ingress Replication, MPLS Label: 12, Leaf Information Required: false, Tunnel ID: 10.1.1.1
BGP routing table entry for imet 10.1.1.1, Route Distinguisher: 10.2.0.1:13
Paths: 1 available
65001
10.1.1.1 from - (0.0.0.0)
Origin IGP, metric -, localpref 100, weight 0, valid, local, best
Extended Community: Route-Target-AS:13:13 TunnelEncap:tunnelTypeVxlan
VNI: 13
PMSI Tunnel: Ingress Replication, MPLS Label: 13, Leaf Information Required: false, Tunnel ID: 10.1.1.1
Primary VLAN
Secondary VLAN
Secondary VLAN
Secondary VLAN
Notes: K

## Slide 27: VXLAN Flood-list
Leaf2#sh vxlan flood vtep
VXLAN Flood VTEP Table
--------------------------------------------------
VLANS Ip Address
---------------------------------------------------
10-13 10.1.1.1
Primary and Secondary VLANs in
VXLAN flood-list
Notes: K

## Slide 28: EVPN Route-Type 2
leaf1#sh bgp evpn route-type mac-ip detail
BGP routing table information for VRF default
Router identifier 10.1.1.1, local AS number 65001
BGP routing table entry for mac-ip 444c.a88d.27c1, Route Distinguisher: 10.2.0.2:10
Paths: 1 available
65002
10.2.1.2 from 10.2.0.2 (10.0.0.1)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ca61, Route Distinguisher: 10.1.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ccf5, Route Distinguisher: 10.1.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
Primary VLAN
Secondary VLAN
Secondary VLAN
Notes: K

## Slide 29: MAC Address and VXLAN Address Table
Leaf2#show vxlan address-table
VLAN Mac Address Type Prt VTEP Moves Last Move
---- ----------- ---- --- ---- ----- ---------
10 985d.82b4.ca61 EVPN Vx1 10.1.1.1 1 0:00:26 ago
10 985d.82b4.ccf5 EVPN Vx1 10.1.1.1 1 0:00:29 ago
Total Remote Mac Addresses for this criterion: 2
Leaf2#show mac address-table
VLAN Mac Address Type Ports Moves Last Move
---- ----------- ---- ----- ----- ---------
10 001c.7300.dc01 STATIC Router
10 444c.a88d.27c1 DYNAMIC Et53/1 1 0:00:10 ago
10 985d.82b4.ca61 DYNAMIC Vx1 1 0:00:07 ago
10 985d.82b4.ccf5 DYNAMIC Vx1 1 0:00:10 ago
Total Mac Addresses for this criterion: 4
MAC Learned in Primary VLAN
MAC Learned in Primary VLAN
Notes: K

## Slide 30: Sand Support for PVLAN with EVPN VXLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Limitation of at most 7 PVLAN domains shared across VTEPs
There is no limitation in numbers of secondary VLANs per primary VLAN
Leaf 1
Leaf 2
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
More Private VLAN Domains can be configured locally, but won’t be able to stretch
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Primary VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Sec. VLAN
Notes: K

## Slide 31: Arista Support for PVLAN with EVPN VXLAN
PVLAN + EVPN/VXLAN supported in 4.26.1F (Quebec) for Trident 3 platforms (7050X3)
PVLAN + EVPN/VXLAN supported in 4.26.2F (Rio) on Jericho/Jericho+ platforms (7280R/R2)
PVLAN + EVPN/VXLAN supported in 4.26.2F (Rio) on Qumran platforms (7020R)
Limitations for Jericho/Jericho+/Qumran platforms:
  Support of maximum 7 stretched private VLANs Domain per switch
  Currently no MLAG support
Notes: A

## Slide 32: Useful Links
PVLAN
  Support for Private VLAN
    https://eos.arista.com/eos-4-25-0f/support-for-private-vlan/
PVLAN over VXLAN/EVPN
  VXLAN Support for Private VLANs on T3
    http://aid.aristanetworks.com/8351/cached.html
  VXLAN Support for Private VLANs over VxLAN tunnels on Sand
    http://aid.aristanetworks.com/8601/cached.html
Notes: A

## Slide 33: Special Thanks
Claus Holbech
Pierre Dezitter
Basil Saji
Milind Kulkarni
Notes: A

## Slide 34: LAB

## Slide 35: Test Agenda
Community VLAN <--> Primary VLAN
Community VLAN X <--> Community VLAN Y
Community VLAN <--> Isolated VLAN
Primary VLAN <--> Isolated VLAN

## Slide 36
s70514
Host 1
s70515
Leaf 1
Spine
s72811
Host 2
E53/1
E27/1
E1
E28/1
172.16.0.1
985d.82b4.ccf5
E33
s70512
Leaf 2
s70513
Host 3
E28/1
E28/1
172.16.0.3
985d.82b4.ca61
E27/1
172.16.0.2
444c.a88d.27c1
10.0.0.0/31
Community VLAN <--> Primary VLAN
H3 in VLAN 12, H1 and H2 in VLAN 10
Leaf
Host
in vlan 10
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13

## Slide 37: VLAN : H3 in VLAN 12, H1 and H2 in VLAN 10
Leaf1#sh vlan
VLAN Name Status Ports
----- -------------------------------- --------- -------------------------------
1 default active
10 VLAN0010 active Cpu, Et27/1+, Et28/1, Vx1
11 VLAN0011 active Cpu, Et28/1+, Vx1
12 VLAN0012 active Cpu, Et27/1, Et28/1+, Vx1
13 VLAN0013 active Cpu, Et28/1+, Vx1
+ indicates a private VLAN promoted port

## Slide 38: Encapsulated Traffic: H3 in VLAN 12, H1 and H2 in VLAN 10
ping H3 → H2 (OK)
15:54:16.254254 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.18655 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 12
98:5d:82:b4:ca:61 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.3 > 172.16.0.2: ICMP echo request, id 16640, seq 1, length 80
15:54:16.254328 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.20406 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 10
44:4c:a8:8d:27:c1 > 98:5d:82:b4:ca:61, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.3: ICMP echo reply, id 16640, seq 1, length 80
ping H2 → H3 (OK)
15:57:22.901888 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.20406 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 10
44:4c:a8:8d:27:c1 > 98:5d:82:b4:ca:61, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.3: ICMP echo request, id 2289, seq 1, length 80
15:57:22.901985 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.18655 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 12
98:5d:82:b4:ca:61 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.3 > 172.16.0.2: ICMP echo reply, id 2289, seq 1, length 80

## Slide 39: EVPN Control-Plane: H3 in VLAN 12, H1 and H2 in VLAN 10
Leaf1(config-if-Et34)#sh bgp evpn route-type mac-ip detail
BGP routing table information for VRF default
Router identifier 10.1.1.1, local AS number 65001
BGP routing table entry for mac-ip 444c.a88d.27c1, Route Distinguisher: 10.2.0.2:10
Paths: 1 available
65002
10.2.1.2 from 10.2.0.2 (10.2.1.2)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ca61, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ccf5, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000

## Slide 40: VXLAN Address Table: H3 in VLAN 12, H1 and H2 in VLAN 10
Leaf2(config)#sh vxlan address-table
Vxlan Mac Address Table
----------------------------------------------------------------------
VLAN Mac Address Type Prt VTEP Moves Last Move
---- ----------- ---- --- ---- ----- ---------
10 985d.82b4.ca61 EVPN Vx1 10.1.1.1 1 0:02:41 ago
10 985d.82b4.ccf5 EVPN Vx1 10.1.1.1 1 0:02:34 ago
Total Remote Mac Addresses for this criterion: 2
H3 is attached to the vlan 12 on the source VTEP but is learned in vlan 10

## Slide 41
s70514
Host 1
s70515
Leaf 1
Spine
s72811
Host 2
E53/1
E27/1
E1
E28/1
172.16.0.1
985d.82b4.ccf5
E33
s70512
Leaf 2
s70513
Host 3
E28/1
E28/1
172.16.0.3
985d.82b4.ca61
E27/1
172.16.0.2
444c.a88d.27c1
10.0.0.0/31
Community 1 VLAN <--> Community 2 VLAN
H1 in VLAN 13, H2 and H3 in VLAN 12
Leaf
Host
in vlan 10
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13

## Slide 42: VLAN : H1 in VLAN 13, H2 and H3 in VLAN 12
Leaf1(config-router-bgp)#sh vlan
VLAN Name Status Ports
----- -------------------------------- --------- -------------------------------
1 default active
10 VLAN0010 active Cpu, Et27/1+, Et28/1+, Vx1
11 VLAN0011 active Cpu, Vx1
12 VLAN0012 active Cpu, Et27/1, Vx1
13 VLAN0013 active Cpu, Et28/1, Vx1
+ indicates a private VLAN promoted port

## Slide 43: Encapsulated Traffic: H1 in VLAN 13, H2 and H3 in VLAN 12
ping H3 → H2 (OK)
16:30:17.181670 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.18655 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 12
98:5d:82:b4:ca:61 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.3 > 172.16.0.2: ICMP echo request, id 18917, seq 1, length 80
16:30:17.181814 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.20406 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 12
44:4c:a8:8d:27:c1 > 98:5d:82:b4:ca:61, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.3: ICMP echo reply, id 18917, seq 1, length 80
ping H2 → H1 (NOK)
16:32:48.107108 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.37622 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 12
44:4c:a8:8d:27:c1 > 98:5d:82:b4:cc:f5, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.1: ICMP echo request, id 6485, seq 1, length 80
There is no echo reply.
ping H1 → H2 (NOK)
16:36:11.517270 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.54434 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 13
98:5d:82:b4:cc:f5 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.1 > 172.16.0.2: ICMP echo request, id 18969, seq 1, length 80
There is no echo reply.

## Slide 44: EVPN Control-Plane: H1 in VLAN 13, H2 and H3 in VLAN 12
Leaf1(config-router-bgp)#sh bgp evpn route-type mac-ip detail
BGP routing table information for VRF default
Router identifier 10.1.1.1, local AS number 65001
BGP routing table entry for mac-ip 444c.a88d.27c1, Route Distinguisher: 10.2.0.2:10
Paths: 1 available
65002
10.2.1.2 from 10.2.0.2 (10.2.1.2)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ca61, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ccf5, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000

## Slide 45: VXLAN Address Table: H1 in VLAN 13, H2 and H3 in VLAN 12
Leaf2(config-macvrf-13)#sh vxlan address-table
Vxlan Mac Address Table
---------------------------------------------------------------
VLAN Mac Address Type Prt VTEP Moves Last Move
---- ----------- ---- --- ---- ----- ---------
10 985d.82b4.ca61 EVPN Vx1 10.1.1.1 1 0:01:51 ago
10 985d.82b4.ccf5 EVPN Vx1 10.1.1.1 1 0:01:56 ago
Total Remote Mac Addresses for this criterion: 2
H3 and H1 are attached to the vlan 12 and vlan 13 respectively on the source VTEP

## Slide 46
s70514
Host 1
s70515
Leaf 1
Spine
s72811
Host 2
E53/1
E27/1
E1
E28/1
172.16.0.1
985d.82b4.ccf5
E33
s70512
Leaf 2
s70513
Host 3
E28/1
E28/1
172.16.0.3
985d.82b4.ca61
E27/1
172.16.0.2
444c.a88d.27c1
10.0.0.0/31
Community VLAN <--> Isolated VLAN
H1 in VLAN 13, H2 and H3 in VLAN 11
Leaf
Host
in vlan 10
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13

## Slide 47: VLAN : H1 in VLAN 13, H2 and H3 in VLAN 11
Leaf1(config-macvrf-11)#sh vlan
VLAN Name Status Ports
----- -------------------------------- --------- -------------------------------
1 default active
10 VLAN0010 active Cpu, Et27/1+, Et28/1+, Vx1
11 VLAN0011 active Cpu, Et27/1, Vx1
12 VLAN0012 active Cpu, Vx1
13 VLAN0013 active Cpu, Et28/1, Vx1
+ indicates a private VLAN promoted port

## Slide 48: Encapsulated Traffic: H1 in VLAN 13, H2 and H3 in VLAN 11
ping H2 → H1 (NOK)
17:08:31.280671 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.37622 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 11
44:4c:a8:8d:27:c1 > 98:5d:82:b4:cc:f5, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.1: ICMP echo request, id 10152, seq 1, length 80
There is no echo reply.
ping H2 → H3 (NOK)
17:25:32.742515 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.20406 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 11
44:4c:a8:8d:27:c1 > 98:5d:82:b4:ca:61, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.3: ICMP echo request, id 12108, seq 1, length 80
There is no echo reply.
ping H2 → H1 (NOK)
17:28:05.119710 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.54434 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 13
98:5d:82:b4:cc:f5 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.1 > 172.16.0.2: ICMP echo request, id 22381, seq 1, length 80
There is no echo reply.

## Slide 49: EVPN Control-Plane: H1 in VLAN 13, H2 and H3 in VLAN 11
Leaf1(config-macvrf-11)#sh bgp evpn route-type mac-ip detail
BGP routing table information for VRF default
Router identifier 10.1.1.1, local AS number 65001
BGP routing table entry for mac-ip 444c.a88d.27c1, Route Distinguisher: 10.2.0.2:10
Paths: 1 available
65002
10.2.1.2 from 10.2.0.2 (10.2.1.2)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ca61, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ccf5, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000

## Slide 50: VXLAN Address Table: H1 in VLAN 13, H2 and H3 in VLAN 11
Leaf2(config-macvrf-11)#sh vxlan address-table
Vxlan Mac Address Table
--------------------------------------------------------------------
VLAN Mac Address Type Prt VTEP Moves Last Move
---- ----------- ---- --- ---- ----- ---------
10 985d.82b4.ca61 EVPN Vx1 10.1.1.1 1 0:02:18 ago
10 985d.82b4.ccf5 EVPN Vx1 10.1.1.1 1 0:02:23 ago
Total Remote Mac Addresses for this criterion: 2
H3 and H1 are attached to the vlan 11 and vlan 13 respectively on the source VTEP

## Slide 51
s70514
Host 1
s70515
Leaf 1
Spine
s72811
Host 2
E53/1
E27/1
E1
E28/1
172.16.0.1
985d.82b4.ccf5
E33
s70512
Leaf 2
s70513
Host 3
E28/1
E28/1
172.16.0.3
985d.82b4.ca61
E27/1
172.16.0.2
444c.a88d.27c1
10.0.0.0/31
Primary VLAN <--> Isolated VLAN
H1 in VLAN 10, H2 and H3 in VLAN 11
Leaf
Host
in vlan 10
Host
in vlan 11
Host
in vlan 12
Host
in vlan 13
Primary VLAN: 10
Isolated VLAN: 11
Community VLAN: 12
Community VLAN: 13

## Slide 52: VLAN : H1 in VLAN 10, H2 and H3 in VLAN 11
Leaf1(config-if-Et28/1)#sh vlan
VLAN Name Status Ports
----- -------------------------------- --------- -------------------------------
1 default active
10 VLAN0010 active Cpu, Et27/1+, Et28/1, Vx1
11 VLAN0011 active Cpu, Et27/1, Et28/1+, Vx1
12 VLAN0012 active Cpu, Et28/1+, Vx1
13 VLAN0013 active Cpu, Et28/1+, Vx1
+ indicates a private VLAN promoted port

## Slide 53: Encapsulated Traffic: H1 in VLAN 10, H2 and H3 in VLAN 11
ping H2 → H1 (OK)
17:55:00.617044 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.37622 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 11
44:4c:a8:8d:27:c1 > 98:5d:82:b4:cc:f5, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.1: ICMP echo request, id 15107, seq 1, length 80
17:55:00.617159 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.54434 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 10
98:5d:82:b4:cc:f5 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.1 > 172.16.0.2: ICMP echo reply, id 15107, seq 1, length 80
ping H1 → H2 (OK)
17:51:58.472818 98:5d:82:b4:dd:f9 > 98:5d:82:c1:6b:03, ethertype 802.1Q (0x8100), length 168: vlan 1006, p 0, ethertype IPv4 (0x0800), 10.1.1.1.54434 > 10.2.1.2.4789: VXLAN, flags [I] (0x08), vni 10
98:5d:82:b4:cc:f5 > 44:4c:a8:8d:27:c1, ethertype IPv4 (0x0800), length 114: 172.16.0.1 > 172.16.0.2: ICMP echo request, id 24100, seq 1, length 80
17:51:58.472944 98:5d:82:c1:6b:03 > 98:5d:82:b4:dd:f9, ethertype IPv4 (0x0800), length 164: 10.2.1.2.37622 > 10.1.1.1.4789: VXLAN, flags [I] (0x08), vni 11
44:4c:a8:8d:27:c1 > 98:5d:82:b4:cc:f5, ethertype IPv4 (0x0800), length 114: 172.16.0.2 > 172.16.0.1: ICMP echo reply, id 24100, seq 1, length 80

## Slide 54: EVPN Control-Plane: H1 in VLAN 10, H2 and H3 in VLAN 11
Leaf1(config-router-bgp)#sh bgp evpn route-type mac-ip detail
BGP routing table information for VRF default
Router identifier 10.1.1.1, local AS number 65001
BGP routing table entry for mac-ip 444c.a88d.27c1, Route Distinguisher: 10.2.0.2:10
Paths: 1 available
65002
10.2.1.2 from 10.2.0.2 (10.2.1.2)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ca61, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000
BGP routing table entry for mac-ip 985d.82b4.ccf5, Route Distinguisher: 10.2.0.1:10
Paths: 1 available
Local
- from - (0.0.0.0)
Origin IGP, metric -, localpref -, weight 0, valid, local, best
Extended Community: Route-Target-AS:10:10 TunnelEncap:tunnelTypeVxlan
VNI: 10 ESI: 0000:0000:0000:0000:0000

## Slide 55: VXLAN Address Table: H1 in VLAN 10, H2 and H3 in VLAN 11
Leaf2(config-macvrf-13)#sh vxlan address-table
Vxlan Mac Address Table
-----------------------------------------------------------------
VLAN Mac Address Type Prt VTEP Moves Last Move
---- ----------- ---- --- ---- ----- ---------
10 985d.82b4.ca61 EVPN Vx1 10.1.1.1 1 0:01:51 ago
10 985d.82b4.ccf5 EVPN Vx1 10.1.1.1 1 0:01:56 ago
Total Remote Mac Addresses for this criterion: 2
H2 and H3 is attached to the vlan 12 and vlan 13 respectively on the source VTEP